Software Safety Requirements and Architecture
Lane Assistance
Document Version: 1.0
Template Version 1.0, Released on 2017-06-21

Document history
Date	Version	Editor	Description
2017-10-19	1.0	Albert Killer	First draft of Software Safety Requirements and Architecture

Table of Contents

Purpose

The purpose of this document is to derive and capture software safety requirements from the technical safety requirements provided by the technical safety concept. Software safety requirements are more specific than technical safety requirements in order to provide precise instructions to the software engineers developing the program. Safety requirements have to be developed while taking into account the vehicle as a whole, otherwise potential hazards could be missed.
Inputs to the Software Requirements and Architecture Document

Technical safety requirements

Technical Safety Requirements related to Functional Safety Requirement 01-01 are:
ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Architecture Allocation	Safe State
Technical / Safety / Requirement / 01	The LDW safety component shall ensure that the amplitude of ‘LDW_Torque_Request’ sent to the ‘Final electronic power steering Torque’ component is below ‘Max_Torque_Amplitude’.	C	50 ms	LDW Safety	LDW_Activation_Status is zero
Technical / Safety / Requirement / 02	The validity and integrity of the data transmission for ‘LDW_Torque_Request’ signal shall be ensured.	C	50 ms	Data Transmission Integrity Check	N/A
Technical / Safety / Requirement / 03	As soon as a failure is detected by the LDW function, it shall deactivate the LDW feature and the ‘LDW_Torque_Request’ shall e set to zero.	C	50 ms	LDW Safety	LDW_Activation_Status is zero
Technical / Safety / Requirement / 04	As soons as the LDW function deactivates the LDW feature, the ‘LDW Safety’ software block shall send a signal to the car display ECU to turn on a warning light.	C	50 ms	LDW Safety	LDW_Error_Status is zero
Technical / Safety / Requirement / 05	Memory test shall be conducted at start up of the EPS ECU to check for any faults in mermory.	A	ignition cycle	Memory Test	LDW_Activation_Status is zero

Refined Architecture Diagram from the Technical Safety Concept

Software Requirements

Lane Departure Warning (LDW) Amplitude Malfunction Software Requirements:

ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Allocation to Architecture	Safe State
Technical / Safety / Requirement / 01	The LDW safety component shall ensure that the amplitude of the LDW_Torque_Request sent to the Final Electronic Power Steering Torque component is below Max_Torque_Amplitude.	C	50 ms	LDW Safety	LDW torque output is setto zero

ID	Software Safety Requirement	ASIL	Allocation Software Elements	Safe State
Software / Safety / Requirement / 01-01	The input signal “Primary_LDW_Torq_Req” shall be read and pre-processed to determine the torque request coming from the “Basic/Main LAFunctionality” SW Component. Signal “processed_LDW_Torq_Req” shall be generated at the end of the processing.	C	LDW_SAFETY_INPUT_PROCESSING	N/A
Software Safety Requirement 01-02	In case the “processed_LDW_Torq_Req” signal has a value greater than“ Max_Torque_Ampltide_LDW” (maximum allowed safe torque), the torque signal “limited_LDW_Torq_Req” shall be set to 0, else “limited_LDW_Torq_Req” shall take the value of “processed_LDW_Torq_Req”.	C	TORQUE_LIMITER	“limited_LDW_Torq_Req” = 0 (Nm=Newton-meter)
Software Safety Requirement 01-03	The “limited_LDW_Torq_Req” shall be transformed into a signal “LDW_Torq_Req” which is suitable to be transmitted outside of the LDW Safety component (“LDW Safety”) to the “Final EPS Torque” component.	C	LDW_SAFETY_OUTPUT_GENERATOR	LDW_Torq_Req= 0 (Nm)

ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Allocation to Architecture	Safe State
Technical / Safety / Requirement / 02	The validity and integrity of the data transmission for LDW_Torque_Request signal shall be ensured	C	50 ms	Data Transmission Integrity Check	N/A

ID	Software Safety Requirement	ASIL	Allocation Software Elements	Safe State
Software Safety Requirement 02-01	Any data to be transmittedoutside of the LDW Safetycomponent (“LDW Safety”)including "LDW_Torque_Req"and “activation_status” (seeSofSafReq03-02) shall beprotected by an End2End(E2E)protection mechanism	C	E2ECalc	LDW_Torq_Req= 0 (Nm)
Software Safety Requirement 02-02	The E2E protection protocol shall contain and attach the control data: alive counter (SQC) and CRC to the data to be transmitted.	C	E2ECalc	LDW_Torq_Req= 0 (Nm)

ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Allocation to Architecture	Safe State
Technical / Safety / Requirement / 03	As soon as a failure is detected by the LDW function, it shall deactivate the LDW feature and the ‘LDW_Torque_Request’ shall e set to zero.	C	50 ms	LDW Safety	LDW_Activation_Status is zero

ID	Software Safety Requirement	ASIL	Allocation Software Elements	Safe State
Software Safety Requirement03-01	Each of the SW elements shall output a signal to indicate any error which is detected by the element. Error signal = error_status_input (LDW_SAFETY_INPUT_PROCESSING), error_status_torque_limiter (TORQUE_LIMITER), error_status_output_gen (LDW_SAFETY_OUTPUT_GENERATOR)	C	All	N/A
Software Safety Requirement03-02	A software element shall evaluate the error status of all the other software elements and in case any one of them indicates an error, it shall deactivate the LDW feature (“activation_status”=0)	C	LDW_SAFETY_ACTIVATION	Activation_status = 0 (LDW function deactivated)
Software Safety Requirement03-03	In case of no errors from the software elements, the status of the LDW feature shall be set to activated (“activation_status”=1)	C	LDW_SAFETY_ACTIVATION	N/A
Software Safety Requirement03-04	In case an error is detected by any of the software elements, it shall set the value of its corresponding torque to 0 so that “LDW_Torq_Req” is set to 0	C	All	LDW_Torq_Req = 0
Software Safety Requirement03-05	Once the LDW functionality has been deactivated, it shall stay deactivated till the time the ignition is switched from off to on again.	C	LDW_SAFETY_ACTIVATION	Activation_status = 0 (LDW function deactivated)

ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Allocation to Architecture	Safe State
Technical / Safety / Requirement / 04	As soons as the LDW function deactivates the LDW feature, the ‘LDW Safety’ software block shall send a signal to the car display ECU to turn on a warning light.	C	50 ms	LDW Safety	LDW_Error_Status is zero

ID	Software Safety Requirement	ASIL	Allocation Software Elements	Safe State
Software Safety Requirement 04-01	When the LDW function is deactivated (activation_status set to 0), the activation_status shall be sent to the car display ECU.	C	LDW_SAFETY_ACTIVATION, CarDisplay ECU	N/A

ID	Technical Safety Requirement	ASIL	Fault Tolerant Time Interval	Allocation to Architecture	Safe State
Technical / Safety / Requirement / 05	Memory test shall be conducted at start up of the EPS ECU to check for any faults in mermory.	A	ignition cycle	Memory Test	LDW_Activation_Status is zero

ID	Software Safety Requirement	ASIL	Allocation Software Elements	Safe State
Software Safety Requirement 05-01	A CRC verification check over the software code in the Flash memory shall be done every time the ignition is switched from off to on to check for any corruption of content.	A	MEMORYTEST	Activation_status = 0
Software Safety Requirement 05-02	Standard RAM tests to check the data bus, address bus and device integrity shall be done every time the ignition is switched from off to on (e.g. walking 1s test, RAM pattern test. Refer RAM and processor vendor recommendations )	A	MEMORYTEST	Activation_status = 0
Software Safety Requirement 05-03	The test result of the RAM or Flash memory shall be indicated to the LDW_Safety component via the “test_status” signal	A	MEMORYTEST	Activation_status = 0
Software Safety Requirement 05-04	In case any fault is indicated via the “test_status” signal the INPUT_LDW_PROCESSING shall set an error on error_status_input (=1) so that the LDW functionality is deactivated and the LDWTorque is set to 0	A	LDW_SAFETY_INPUT_PROCESSING	Activation_status = 0

Refined Architecture Diagram